## Slide 1
Runtime-adaptive scratchpad buffering
01 / 24
RTL implementation and controlled performance study
University VLSI laboratory review • 14 functional tests • 129 simulations

## Slide 2
Research questions
02 / 24
When does deeper multi-bank buffering outperform fixed two-bank ping-pong?
Can a runtime bank limit retain fixed four-bank performance with fewer eligible banks?

## Slide 3
Memory-induced MAC stalls
03 / 24
Tile source
Transfer interface
Scratchpad banks
MAC engine
The MAC waits whenever no completed tile is READY.

## Slide 4
Scratchpad model and tiling
04 / 24
Each tile contains activation and weight pairs; the MAC verifies their product sum.
Synchronous behavioral RAM represents an RTL scratchpad architecture.
Effective tile transfer cycles abstract slower memory latency; no physical SRAM or DRAM protocol is modeled.

## Slide 5
Relevant prior accelerator work
05 / 24
Eyeriss: distributed local storage and row-stationary reuse.
TPU: large software-controlled on-chip memory with systolic compute.
Eyeriss v2: flexible network for varying layer shapes and sparse data.
Notes: Sources: https://doi.org/10.1109/JSSC.2016.2616357 ; https://arxiv.org/abs/1704.04760 ; https://doi.org/10.1109/JETCAS.2019.2910232

## Slide 6
Published results: conditions matter
06 / 24
Paper | Workload and platform | Published metric
Eyeriss | AlexNet conv., batch 4, ASIC | 35 frames/s; 0.0029 DRAM accesses/MAC
TPU | Production datacenter inference, ASIC | ~15–30× vs its CPU/GPU
Eyeriss v2 | Sparse MobileNet, batch 1, 65 nm | 1470.6 inferences/s; 12.6× vs Eyeriss
Notes: Source values: IEEE JSSC Eyeriss DOI 10.1109/JSSC.2016.2616357; TPU ISCA DOI 10.1145/3079856.3080246; Eyeriss v2 JETCAS DOI 10.1109/JETCAS.2019.2910232. All comparisons here qualitative.

## Slide 7
Cross-paper comparability
07 / 24
Our measured unit is cycles to complete a specified synthetic tile stream.
Published frame rates, inference rates, energy, and speedups use different workloads and hardware.
Therefore the published comparison is QUALITATIVE; controlled RTL baselines answer the scheduling question.
Notes: Same primary sources as slide 6. The published metrics and baselines cannot be converted to our tile-cycle metric.

## Slide 8
Single-buffer baseline
08 / 24
LOAD tile
COMPUTE tile
LOAD next tile
A bank cannot load while its tile is computing.

## Slide 9
Fixed two-bank ping-pong
09 / 24
LOAD A
COMPUTE A + LOAD B
COMPUTE B + LOAD A
Tile IDs alternate between A and B.

## Slide 10
Fixed four-bank availability baseline
10 / 24
EMPTY search
READY queue
MAC dispatch
Four banks are always eligible for new tile allocation.

## Slide 11
Static cyclic multi-bank proxy
11 / 24
A tile's bank is fixed by tile ID modulo four; compute dispatch stays in tile order.
This is a generic literature-inspired RTL scheduling proxy, not an exact reproduction of a published accelerator.
It shares the same RAM, MAC, workload, and simulator as the proposed policy.

## Slide 12
Limitation of fixed buffering depth
12 / 24
Stable compute-bound workloads often need only two eligible banks.
A fixed four-bank controller offers no extra cycle benefit in the measured steady 8/8 and 8/20 cases.
The new mechanism changes allocation eligibility according to observed starvation.

## Slide 13
Runtime depth architecture
13 / 24
Stall statistics
Hysteresis control
Limit 2 / 3 / 4
Existing scheduler
Four physical banks remain. A lower limit blocks new allocation only; in-flight tiles drain.

## Slide 14
Bank state machine
14 / 24
EMPTY
LOADING
READY
COMPUTING
MAC completion returns a bank to EMPTY.

## Slide 15
Hysteresis and starvation observation
15 / 24
Observation window: 32 clocks. A stall event requires unfinished work, an available MAC, and no READY bank.
Stalls ≥ 8: 2→3→4. Stalls ≤ 2: 4→3→2. Other windows keep the current mode.
Integer comparisons avoid RTL division. Average limit is an effective buffering-depth metric, not measured power.

## Slide 16
Verification record
16 / 24
Gate | Observed result
Functional correctness | 14 / 14 PASS; every tile MAC and ID checked
Performance sweep | 129 / 129 STATUS=PASS
Regression preservation | 103 old runs: seven core metrics unchanged
Analytical checks | 129 cycle/accounting checks; 6 VCD transitions
Notes: Source: results/raw/*.log; scripts/analyze_results.py; docs/analytical_checks.md.

## Slide 17
Fixed latency: buffering overlaps work
17 / 24
Chart: Total cycles
| 8/8 | 16/16 | 32/32
Single | 640 | 1152 | 2176
Ping-pong | 361 | 625 | 1153
Fixed 4 | 361 | 625 | 1153
Notes: Source: results/csv/fixed_latency_results.csv, 32 tiles, tile size 4, base 8/8.

## Slide 18
Variable latency: a third bank helps
18 / 24
Chart: Total cycles
| Single | Ping-pong | Fixed 4
Total cycles | 922 | 539 | 497
Fixed four-bank speedup over ping-pong: 539 / 497 = 1.0845×
Notes: Source: results/csv/variable_latency_results.csv; 32 tiles; deterministic base 8/8 pattern.

## Slide 19
Bank scaling saturates at three
19 / 24
Chart: Total cycles
| 2 | 3 | 4 | 6 | 8
Total cycles | 539 | 497 | 497 | 497 | 497
Notes: Source: results/csv/bank_scaling_results.csv; 32 tiles; variable base 8/8.

## Slide 20
Stable workloads retain fixed-four timing
20 / 24
Chart: Total cycles
| Compute-bound | Balanced
Fixed 4 | 1481 | 713
Runtime | 1481 | 713
Runtime average limit: 2.022 and 2.045 banks
Notes: Source: results/csv/adaptation_results.csv; 64 tiles; compute 8/20 and balanced 8/8.

## Slide 21
Variable timing exposes a tradeoff
21 / 24
Chart: Total cycles
| Ping-pong | Fixed 4 | Runtime
Total cycles | 1072 | 983 | 1025
Runtime: 4.27% more cycles than fixed 4; average limit 2.50
Notes: Source: results/csv/adaptation_results.csv; 64 tiles, deterministic variable base 8/8.

## Slide 22
Phase change: measured mode waveform
22 / 24
2033 runtime vs 1991 fixed-four cycles; average limit 2.582 banks
Notes: Source: results/waveforms/adapt_phase_runtime_adaptive.vcd, parsed by scripts/analyze_results.py. The image is waveform-derived, while quantitative bar charts elsewhere remain native editable objects.

## Slide 23
Equal physical word count
23 / 24
Scenario (16 total RAM words) | Ping-pong 2×8 | Fixed 4×4 | Runtime 4×4
Variable, 64 tiles | 1072 | 983 | 1025
Phase, 96 tiles | 2054 | 1991 | 2033
Notes: Source: results/csv/equal_storage_results.csv. Extra ping-pong words cannot hold another tile in the implemented controller.

## Slide 24
Measured conclusion and limits
24 / 24
Four-bank capacity helps under the tested variable timing; the static four-bank proxy matches availability scheduling here.
Runtime depth matches fixed-four time in stable cases and averages near two eligible banks.
Under changing timing it averages 2.50–2.58 banks with 2.11–4.27% more cycles. No physical power benefit was measured.